MATERIAL SAFETY   DATA   SHEET

Product: XYLENE	Page 1 of 4		Date of Issue: November 2007

Hazardous according to criteria of Worksafe Australia

1	PRODUCT & COMPANY UNDERTAKING IDENTIFICATION

Product Name:				Xylene

Major Recommended Use: 		Thinners and cleanup solvent for Auseal products

Company:					Auseal – Curite Pty. Ltd.

ABN:						33 084 155 242

Address:					25 – 29 Pelson Court, Dandenong. Victoria   3175

Telephone Number:			61 (03) 8787 8388

Fax Number:				61 (03) 8787 8366

Email:						auseal1@optusnet.com.au

2	COMPOSITION/INFORMATION ON INGREDIENTS

Chemical Name					CAS Number		Proportion		Classification

Xylene						1330-20-7			100%			R20/21	R38

Description		Flammable Liquid

3	HAZARDS IDENTIFICATION

Harmful by inhalation and in contact with skin (R20/21).

Irritating to skin. (R38).

SUSDP:	6

ADG CLASS:	3

Signs and Symptoms of Exposure (Acute effects):

Swallowed:		Ingestion may cause: severe gastrointestinal irritation, headache, nausea, vomiting. Small amount of liquid aspirated into respiratory system during ingestion or vomiting may cause bronchopneumonia or pulmonary oedema.

Eye:	Contact with eyes can cause mild irritation and discomfort, and may cause conjunctivitis and corneal oedema when absorbed into the tissue of the eye from the atmosphere.  Corneal oedema may give rise to a perception of blue haze or fog around lights.  This effect is transient and has no known residual effect.

Skin:	Irritating to skin. Absorption through skin may occur resulting in harmful effects or illness. Prolonged and repeated contact may result in skin sensitisation and dermatitis due to de fatting.

Inhaled:	Prolonged inhalation may result in respiratory irritation, dizziness, nausea, and loss of consciousness. Aspiration into the lungs may cause chemical pneumonitis which can be fatal.

Chronic:	Repeated and/or prolonged exposures may result in: adverse skin effects (de fatting, rash or allergic reaction/sensitisation), adverse eye effects (conjunctivitis) and temporary liver or kidney damage.

4	FIRST AID MEASURES

Swallowed:	If swallowed, do NOT induce vomiting, Give a glass of water and contact a doctor or Poisons Information Centre. Phone 131126.

Eye:	Immediately hold eye open and irrigate with water for 15 minutes. If persistent irritation occurs, obtain medical attention and see a Doctor.

Skin:	Remove any contaminated clothing and product.  Wash skin thoroughly with mild 	soap/water.  Seek medical advice if ill effect or irritation develops.

Inhaled:	Using proper respiratory protection, immediately remove the affected victim from exposure to fresh air.  If breathing is laboured and patient is cyanotic (blue), ensure airways are clear and have qualified person give oxygen through a face mask. If breathing has stopped apply artificial respiration at once. In the event of cardiac arrest, apply external cardiac massage. Seek immediate medical advice.

First Aid Facilities:	Eyewash fountains and safety showers should be available for emergency use.

Advice to Doctor:	Dermatitis may result from prolonged or repeated exposure.

Aspiration into the lungs may cause chemical pneumonitis. Causes central nervous system depression. Severe exposure may cause blurred vision, tremors, shallow and rapid breathing, delirium and unconsciousness.

Product: XYLENE	Page 2 of 4		Date of Issue: November 2007

5	FIRE FIGHTING MEASURES

Suitable Extinguishing Media: Ignition will give rise to a Class B fire. In case of large fire use: water spray, alcohol foam. In case of small fire use: Foam. Dry chemical powder, carbon dioxide, sand or earth.

Special Exposure Hazards (fire fighting): Carbon monoxide may be evolved if incomplete combustion occurs. Will float and can be reignited on surface water. The vapour is heavier than air, spreads along the ground and distant ignition is possible.

Special Fire Fighting Procedures: Fire fighters should wear full protective clothing and self-contained breathing     apparatus. Water spray should be used to cool intact drums. Prevent runoff from fire control entering waterways.

6	ACCIDENTAL RELEASE MEASURES

Precautions: Eliminate all sources of ignition. Wear protective clothing, boots, gloves, and eye protection.

Methods for Cleaning Up: If recovery is not feasible, admix with dry soil, sand or non reactive absorbent and place in an appropriate chemical waste container. Transfer to containers by suction, preparatory for later disposal. Flush area with water spray. Clean up personnel must be equipped with self contained breathing apparatus and butyl rubber protective clothing. For large spills, recover spilled material with vacuum truck.

7	HANDLING & STORAGE

Handling: Avoid skin and eye contact and inhalation of vapours. Wear overalls, chemical goggles and impervious gloves. Use with adequate ventilation. If inhalation risk exists wear organic vapour respirator meeting the requirements of AS 1715 and AS 1716. Always wash hands before smoking, eating, drinking or using the toilet. Wash contaminated clothing and other protective equipment before storage or reuse.

Storage: Flammable Liquid (Class 3). Take precautionary measures against static discharge. Store in well ventilated area. Store away from organic, combustible materials, oxidizing agents, foodstuffs. Keep containers closed at all times. Check regularly for leaks. Avoid thermal shock. Store in cool place and out of direct sunlight. Store away from sources of heat or ignition.

8	EXPOSURE CONTROLS/PERSONAL PROTECTION

Exposure Standards:	TWA (8 h) = 100 ppm   TWA (8 h) = 441 mg/m3

STEL (15 min) = 150 ppm  STEL (15 min) = 662 mg/m3   Can be absorbed through the skin

Engineering Controls:	Use local exhaust ventilation

Hand Protection:	Wear impervious gloves if contact with liquid is possible. Viton offers good resistance; other materials may be less suitable. Check with equipment supplier to determine if level of protection is adequate.                          Eye Protection:	Splash proof eye goggles.

Body Protection:	Standard issue work clothes safety shoes or boots - chemical resistant. If splashes are likely to occur, wear: long sleeve overall. Check with equipment supplier to determine if level of protection is adequate.

Flammability:	Flammable

9	PHYSICAL & CHEMICAL PROPERTIES

Appearance:					Clear colourless liquid

Smell:							Aromatic Solvent

pH:							No data

Boiling Point (@760mm Hg):			Typical 138.7 – 142.3°C  (ASTM D-1078)

Melting Point:					No data

Flashpoint (°C):					Typical 25°C (Abel)

Flammability:					Flammable

Explosive Limits:					LEL: 1.10 %v/v	UEL: 6.60% v/v

Auto - ignition Temperature:			= 500 °C (ASTM E-659)

Explosive Properties:				No data

Explosive Limits:					No data

Oxidising Properties:				No data

Vapour Pressure (kPa @ 20°C):		1

Vapour Density (Air =1):				3.7

Solubility in Water:					Insoluble

Specific Gravity:					0.87

Per cent Volatiles:					100%

10	STABILITY & REACTIVITY

Stability: Stable under normal use conditions. Reacts with strong oxidising agents. Reacts with strong acids.               Conditions to Avoid: Heat, sparks, flames.

Incompatibility (Materials to Avoid): Strong acids. Strong oxidising agents

Hazardous Decomposition Products: None known.

Hazardous Transformation Products: Will not occur.

Product: XYLENE	Page 3 of 4		Date of Issue: November 2007

11	TOXICOLOGICAL INFORMATION

No product toxicological information is available, but similar product they are as follows:

Acute Oral Toxicity (LD50,): Low toxicity, LD50 > 2000 mg/kg

Acute Dermal Toxicity (LD50,): Low toxicity, LD50 > 2000 mg/kg

Acute Inhalation Toxicity (LC50,): Low toxicity, LD50 > 5 mg/L

12	ECOLOGICAL INFORMATION

Basis for assessment:	Ecotoxicological data have not been determined specifically for this product.

The information given below is based on knowledge of the components and the ecotoxicology of similar products.

Mobility:			Floats on water. Evaporates within a day from water or soil surfaces.

Dissolved material evaporates rapidly.

Product remaining on soil surface evaporates within a day.

If product enters soil, it will be mobile and may contaminate groundwater.                               Persistence/

degradability: 		Readily biodegradable.

Expected to persist under anaerobic conditions.

Oxidises rapidly by photo-chemical reactions in air.

Integrated environmental half-life expected to be < 1 day.

Dominant loss process - photolysis.

Expected to pose a significant risk of oxygen depletion in aquatic systems.

Bioaccumulation: 	Does not bioaccumulate significantly.

Acute toxicity – fish:			Toxic, 1 < LC/EC/IC 50 <= 10 mg/l .

Acute toxicity - invertebrates:		Toxic, 1 < LC/EC/IC 50 <= 10 mg/l .

Acute toxicity – algae:			Toxic, 1 < LC/EC/IC 50 <= 10 mg/l .

Acute toxicity – bacteria:		Slightly toxic, 10 < LC/EC/IC 50 <= 100 mg/l . Based on o- and p-xylene.

Sewage treatment:	Expected to be not toxic at limit of water solubility.

Other information:	In view of the high rate of loss from solution, the product is unlikely to pose a significant hazard to aquatic life. Based on product composition.

13	DISPOSAL CONSIDERATIONS

Precautions: 		Refer to Section 7 before handling the product or containers.

Waste disposal: 		Recover or recycle if possible. Otherwise: Incineration.

Product disposal: 	Recover or recycle if possible. Otherwise: Incineration.

Container disposal: 	Drain container thoroughly. After draining, vent in a safe place away from sparks and fire. Residues may cause an explosion hazard. Do not puncture, cut or weld uncleaned drums. Send to drum recoverer or metal reclaimer.

Local legislation: 	The recommendations given are considered appropriate for safe disposal. However, local regulations may be more stringent and these must be complied with.

14	TRANSPORT INFORMATION

SHIPPING NAME: XYLENES,  (Flammable  Liquid)

Packing Group: III

| Mode | Regulations | Class | Packaging Group | Notes |
| --- | --- | --- | --- | --- |
| - | UN | 1307 | III |
|  | Sea | IMDG | Class 3.3 | III |
|  | Road/Rail | ADG Code | Class 3 | III |
|  | Air | IATA/ICAO | Class 3 | III |

Classified as a 3 (FLAMMABLE LIQUID) Dangerous Substance for the purpose of transport. Refer to relevant regulations for storage and transport requirements.

Not to be loaded with explosives (Class 3), spontaneously combustible substances (Class 4.2), oxidising agents (Class 5. 1) organic peroxides (Class 5.2), foodstuff empties, however exemptions may apply.

This material is a Scheduled Poison (S6) and must be stored, maintained and used in accordance with the relevant regulations.

Product: XYLENE	Page 4 of 4		Date of Issue: November 2007

15	REGULATORY INFORMATION

EEC Symbol: Xn (HARMFUL), Xi (IRRITANT), F (Flammable)

EEC Council Directives relating to the classification, packaging and labelling of dangerous substances and preparations Risk (R) and Safety (S) phrases:

R10  			 Flammable

R20/21 	 		 Harmful by inhalation and in contact with skin

R38 	 		 Irritating to skin

S2				 Keep out of reach of children

S9				 Keep container in a well ventilated place

S16				 Keep away from sources of ignition – No smoking

S23				 Do not breathe vapour

S24/25			 Avoid contact with skin and eyes

16	OTHER INFORMATION

Uses and restrictions:	Raw material for use in the chemical industry. Persistent abuse involving repeated and prolonged exposures to high concentrations of vapour ('sniffing') has been reported to result in central nervous system damage and eventually death.

MSDS distribution:	The information in this document should be made available to all who may handle the product.

Reference:	The content and format of this safety data sheet is in accordance with Commission Directive 93/112/EC of 10 December 1993 amending Commission Directive 91/155/EEC.

The information in this SDS was obtained from sources which we believe are reliable.  However, the information is provided without warranty, express or implied, regarding its correctness.  The conditions or methods of handling, storage, use or disposal of the material are beyond our control and may be beyond our knowledge.  For this and other reasons, we do not assume responsibility and expressly disclaim liability for loss, damage or expense arising from or in any way connected with the handling, storage, use or disposal of the material